1.3.2. Tender text

.......... units

Rotary floor twist outlet for floor installation with high induction effect in floor zone, thus quick decrease in jet velocity and intensive energy exchange with ambient air;

air jet axis approx. at 30° incline to the vertical and rotatable air outlet element for individual adjustment of air jet direction or air flow intensity at workplace;

air outlet can be walked over, driven over and can support a wheel chair;

consisting of:

- circular twist element with radial and circular slots and textured surface,

for DN 125:

- Distributor insert with slots including throttle device for reduction of supply air flow rate as required with clamp insert for installation in through bore of floor tile, with rotary claw.

for DN 200, different options of distributor basket:

- Standard distributor basket with slots and optional throttle device for reduction of supply air flow rate as required.

- Short distributor basket with slots for raised floors with lower plenums, without throttle device.

- Low distributor basket with slots and openable bottom, best for raised floors with thicker tiles and lower plenums, with optional throttle device for reduction of supply air flow rate as required.

- Perforated sheet metal distributor basket, including throttle device for reduction of supply air flow rate as required.

- Short type with fixed damper for even supply air distribution when used in assembly rooms or with low air outlet volume flow rates.

- with clamp insert for installation in through bore of floor tile, optionally fitted with clamp nut 2), clamp collar, or claw fastener.

- Optional connection box for connection of air outlet to a flexible duct.

Material:

- Twist element and clamp insert made of polycarbonate, body-tinted in a colour similar to RAL 7037, dust grey 3), or made of aluminium (only DN 200) in natural colour 3).

- Distributor baskets VD, VSD, VK and VND made of polycarbonate, body-tinted in a colour similar to RAL 9005, jet-black

- Distributor basket VPD made of sheet metal

- Distributor basket VL made of polycarbonate, body-tinted in a colour similar to RAL 9005, jet-black; damper made of sheet metal

- Connection box made of galvanized sheet metal.

Make: Krantz

Type: DB-D __ – DN___ – __ __ – __ – __

Subject to technical alterations.

2) Only for plastic outlet

3) Other colour on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de