1.3.3. Tender text 1)

.......... units

Adjustable floor outlet,

suitable as floor twist outlet for generating high-turbulence vertical

flow or as a floor displacement outlet for low-turbulence, radial

horizontal flow,

installed in conventional raised floor systems,

Air outlet can be walked over, driven over and can support a wheelchair

consisting of:

- Discharge element with radial discharge slots and built-in adjustment device for mode selection from floor twist outlet to floor displacement outlet operation and vice versa, structured surface,

- optional “Standard distributor basket” with surrounding slots in basket casing, optional including throttle device or „Short distributor basket” with surrounding slots in basket casing, best for low raised floors; without throttle device,

- Clamp insert for installation in through bore of floor tile, optional with clamp nut or with claw fastener,

- Connection box for direct connection of air outlet unit to a flexible tube, optional with volume flow damper, adjustable from room.

Material:

- Air outlet element made of polycarbonate, colour of visible air outlet parts coloured similar to RAL 7037, dust grey 2)

- Clamp insert made of polycarbonate, colour of visible air outlet parts coloured similar to RAL 7037, dust grey 2)

- Distributor basket made of polycarbonate

- Connection box made of galvanized sheet metal

Make: Krantz

Type: BA-V – DN 150 – ___ __ – __ – __

Subject to technical alterations.

1) For the required air outlet type (kind, material, etc.) or possible combination of individual components see Technical Selection table on page 5, “Types available” 
2) other colours on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de