1.1.10.2. Tender text

… units

Circular Opticlean with horizontal air discharge, for installation in suspended ceiling systems made from mineral fibre or gypsum board, designed to generate a high-quality indoor air flow at low air velocities and uniform air temperatures; unobtrusive integration into the suspended ceiling; strong reduction of dirt accumulation on the ceiling thanks to very uniform air discharge and formation of an air cushion; also usable as return air inlet;

outlet consisting of:

- circular faceplate with round staggered perforations, 3 mm in diameter, and collar

- air distribution element with top connection spigot for connection to a flexible duct

- optional connection box with lateral connection spigot and suspension brackets, optionally fitted with volume flow damper adjustable at the spigot.

Materials:

- Faceplate made of galvanized sheet metal painted to RAL ....

- Air distribution element made of aluminium

- Connection box made of galvanized sheet metal

Make: KRANTZ KOMPONENTEN

Type: OC – R – ___ / _ _ – ____

Subject to technical alteration.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de