1.2.2. Tender text – – Supply air outlet

.......... units

Radial slot outlet generating high-induction radial air jets for high-quality indoor air flow, with symmetrical or asymmetrical air discharge, for installation flush with ceiling or freely suspended,

consisting of:

- outlet element with circular face and radial, linear slots, discharge direction 4-sided, 3-sided, 2-sided or 2-sided symmetrical asymmetrical; including central fastening screw with cap,

- circular connection box with built-in central fastening for the outlet element, either cubical or circular, suspension brackets on the top, lateral connection spigot with built-in volume flow damper adjustable from room.

Material:

- Outlet element made of galvanized sheet metal, powder-coated, with face painted to RAL 9010, pure white 1)

- Blades made of polycarbonate PC GF 10, body-tinted similar to RAL 9005, jet-black, or RAL 9010, pure white

- Connection box made of galvanized sheet metal

Make: Krantz

Type: RL-C2 __ – ___ – Z __ – __ – ____ – __

1.2.2. Tender text – – Return air outlet

.......... units

Radial slot outlet as return air inlet,

for installation flush with the ceiling or freely suspended,

consisting of:

- outlet element with circular face and radial, linear slots, either with or without blades; including central fastening screw with cap,

- circular connection box with built-in central fastening for the

- outlet element, either cubic or circular, suspension brackets on the top, lateral connection spigot with built-in volume flow damper adjustable from room.

Material:

- Outlet element made of galvanized sheet metal, powder-coated, with face painted to RAL 9010, pure white 1)

- Blades made of polycarbonate PC GF 10, dyed similar to RAL 9005, jet-black, or RAL 9010, pure white

- Connection box made of galvanized sheet metal 2)

Make: Krantz

Type: RL-C2 __ – ___ – A __ – __ – ____ – __

Subject to change without notice.

1) other colours on request
2) On request the connection box is painted black internally

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de