1.6.3. Tender text – Linear step displacement outlet

.... units

Linear step displacement outlet Q–SL, for installation in a step cutout or bore, designed for low-turbulence, draught-free fresh air supply to the occupied zone,

consisting of:

- finely perforated frontal plate to generate low-turbulence discharge flow according to the principle of displacement ventilation,

- perforated intake or fixed throttle for even air supply, especially when several outlets are connected to the floor plenum,

- Air intake from pressurized plenum, intake at the back or the bottom of the outlet, jet straightener to raise jet on discharge side, optionally with frame and screws or claw fasteners 1), or without frame, with fixing brackets for push-in connection,

- skirting seal for ensuring airtightness.

- optional template for fastening type B (with fixing brackets)

Material

- Step displacement outlet made of galvanized sheet metal,visible part painted to RAL ....

- Jet straightener made of polycarbonate PC GF 10, dark grey

Technical data

Volume flow rate: ...................................l/s (m3/h)

Perm. sound power level:.....................dB(A)

Pressure loss: ....................................Pa

Height / Length: 120 mm /...................................mm

Make: Krantz

Type: Q-SL – ____ – ____ – __ – __ – ____

1.6.3. Tender text – Circular step displacement outlet

.... units

Circular step displacement outlet Q–SR for installation in a step cutout or bore, designed for low-turbulence, draught-free fresh air supply to the occupied zone,

consisting of:

- finely perforated frontal plate to generate low-turbulence discharge flow according to the principle of displacement ventilation,

- perforated intake or fixed throttle for even air supply, especially when several outlets are connected to the floor plenum, air intake from pressurized plenum,

- skirting seal at the back of the exit flange to ensure airtightness,

- concealed hexagon socket screws at claw fasteners.

Material

Step displacement outlet made of galvanized sheet metal, visible part painted to RAL ....

Technical data

Volume flow rate: ........................ l/s (m3/h)
Perm. sound power level: .....................dB(A)
Pressure loss: .....................Pa
Size: DN.......... ...........

Make: Krantz

Type: Q-SR – DN ____ – ____

Subject to technical alterations.

1) Colourless cap; RAL colour on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de