2.5.2.4 Tender text

..... units

Rectangular floor displacement outlet generating a combined mixing/displacement flow or hybrid flow as described in German VDI 3804 guideline, for mounting in a raised floor,

consisting of:

- a housing with two supply air connections; the housing walls are bevelled to receive the walkable grille; to make up for constructional tolerances the air outlet is fitted with threaded screws that are adjustable in height;

- a perforated air distribution plate (non-adjustable) which creates the hybrid flow;

- a linear bar grille, stiff and walkable (optional designs: crossbar grille, roll-up grille), bar dimensions: 16 x 5 mm, bar spacing: 8.5 mm. The support frame is fixed to the outlet housing by means of turnable clips.

Material:

- Housing made of galvanized sheet metal painted to RAL 7024 (graphite grey), matt

- Grille and support frame made of aluminium anodized in natural colour (other anodization colours or RAL colour finishes on request).

Make: KRANTZ KOMPONENTEN

Type: Q-BR-____ / ___ / ___ - _____ / __ – ___

Subject to technical alteration.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de