1.5.3.1. Tender text – Trapezoidal displacement outlet

.......... units

with little induction effect for minimum mixing of supply air with indoor air so as to achieve optimum displacement of dust particles and pollutants from the occupied zone, air downflow,

consisting of:

- Nominal width 140	
Housing with trapezoidal, perforated discharge surface to be pulled down for cleaning, and top rectangular spigot for duct connection, with flange and built-in volume flow damper adjustable from outside.	
Placement can optionally be free-hanging, flush with the ceiling

or along a wall

- Nominal widths 290 and 500	
Housing with trapezoidal, perforated discharge surface and built-in twist outlets; housing with hinges that can be pulled down for cleaning purposes; the top rectangular spigot for duct connection with built-in volume flow damper, which is adjustable from the outside; and insertion frame.	
Placement can optionally be free-hanging or flush with the ceiling.

Material:

- Housing and perforated plate made of galvanized sheet metal, optional painted to RAL ....

- Twist outlets 1) made of polystyrene

Make:	Krantz

Type:	VA – T – _____ / _____ – __

Subject to technical alteration.

1) Only for nominal widths 290 and 500

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de