1.5.4. Tender text

........ units

Swivel displacement outlet with low induction effect and minimal mixing of supply air with indoor air for optimum displacement of dust particles and pollutants from the occupied zone,

consisting of:

- housing for duct connection, built-in swivel air distribution element with large front panel made up of a perforated plate and built-in twist outlets,

- swivel mechanism to change the direction of air flow from +10° to –35° to the horizontal, positioned to the right or left of the housing (related to air flow); adjustment options: manual device or electric servomotor.

Material:

- Housing and perforated plate made ofgalvanized sheet metal

- Twist outlets made of polystyrene, hardly inflammable (class B1 to DIN 4102-1)

Make: KRANTZ KOMPONENTEN

Type: VA – S ….

Subject to technical alterations.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de