1.5.5. Tender text Radial displacement outlet VA-PV

… units
Radial displacement outlet for vertical low-turbulence supply air distribution above the occupied zone into the gangways of production facilities, especially suited for workplaces with extract points; discharge direction continuously adjustable from inclined to steeply downwards, preferably in response to temperature difference between supply air and indoor air,

consisting of:

- an outer cylinder, an air dispersion element, a core tube for a support jet, and a perforated metal sheet for low-turbulence air discharge,

- an oval adjustable damper for support jet regulation and alteration of jet spread and penetration depth; damper adjustment via manual device, electric actuator, or self-acting thermostatic control unit.

Outlet connection to circular duct or connection box with lateral spigot.

Material:

- Cylindrical and circular outlet parts made of aluminium; visible parts painted to RAL …

- Perforated metal sheet and baffle made of galvanized sheet metal

- Connection box made of galvanized sheet metal.

Make: KRANTZ KOMPONENTEN

Type: VA-PV – DN ____ – __ – ___ – ____

Subject to technical alterations.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de