1.2.1.2. Tender text Combined multiplex outlet FA-VK

… unit 
Multiplex outlet for flush installation in the upper area of a room wall, with rectangular housing; rear air connection via connection spigot 1) fitted with damper adjustable from the room side;

types available:

- Combined multiplex outlet for supply and return air with common front plate, either non-perforated, with round jet bundle elements in lower supply air and upper return air segments; supply air discharge and return air intake through jet bundle elements;
or perforated, with round jet bundle elements in lower supply air segment; supply air discharge through jet bundle elements, return air intake through free perforations in upper return air segment.
Jet bundle elements for supply air manually and individually rotatable for air jet spread as desired by altering the discharge direction; rapid decrease in jet velocity and temperature difference supply air to indoor air.

Material:

- 2-part jet bundle elements (nozzle discs) 
– Orifice disc made of polycarbonate PC-GF-10-V0 bodytinted in a colour similar to RAL 9010, pure white, or similar to RAL 9005, jet-black 2)
– Nozzle support made of acrylonitrile-butadiene-styrene ABS-V0 body-tinted in a colour similar to RAL 9005, jet-black

- Housing and front plate made of galvanized sheet metal, visible part of front plate painted to RAL 9010, pure white 2)

Make: KRANTZ KOMPONENTEN

Type: FA – VT-__ __ – __ – ___ – ___ – __

Subject to technical alteration.

1) With lip sealing on request
2) Other colours on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de