1.2.9. Tender text

… unit 
Crosstalk attenuation air transfer element with built-in crosstalk silencer for mounting in plasterboard walls, for reduction of sound transmission from one room to the adjacent one,

element consisting of:

- housing available either with staggered openings (S-shape) or with opposite openings on one level (T-shape), with built-in crosstalk silencer

- optional front plate on each side, fitted with round perforations
or rectangular slots; easy fastening with clip connections

Material:

- Housing made of galvanized sheet metal

- Crosstalk silencer made of abrasion-resistant acoustic lining (Basotect) of fire resistance class B1 to DIN 4102-1

- Front plate made of galvanized sheet metal powder coated to RAL 9010, pure white

Make: KRANTZ KOMPONENTEN

Type: OG

Subject to technical alterations.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de