2.2.2. Tender text

..... units

Contact cooling ceiling system KKS-4/GK consisting of single, compact cooling elements for mounting in gypsum board ceilings. Each element is composed of:

- serpentine pipework made from copper tube 12 x 0.35 mm featuring a smooth, neat and dry inside surface, copper to DIN 1787 and pipework tolerances to DIN 8905, with connection ends for chilled water inflow and outflow,

- an aluminium heat conducting plate with aluminium pipe saddles to bond the pipework to the aluminium plate and optimize thermal conduction between copper and aluminium,

- suspensions.

The KKS-4/GK elements are hooked to the furring channels of the ceiling suspension structure using specially shaped suspensions.

The exact arrangement of the elements along with all dimensions and the information plotted on the architect’s ceiling layout are part of our design work and delivery.

Technical data

Specific cooling output: 		 W/m2

Cooling output of each element: 		 W

Water supply temperature: 		 °C

Water return temperature: 		 °C

Room temperature: 		 °C

Max. operating pressure (standard): 	6 bars

Water quality: 	mains water

Standard dimensions

Nominal width: 	unperforated: 420 mm

perforated: 	250 mm

Nominal length: 		 mm

Connection type

Pipe end for press fitting: 	dia 12 mm

Make: 	KRANTZ KOMPONENTEN

Type: 	KKS-4/GK / __ – ____

Subject to technical alteration.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de