2.4.2. Tender text Chilled beam DK-LIG/Z – __ – __ – 600

… units

Active chilled beam for cooling and heating indoor air with simultaneous fresh air supply (centrally conditioned primary air), particularly suitable for installation in closed suspended ceilings instead of a standard ceiling tile,

consisting of:

– a rectangular housing with primary air spigot,

– primary air nozzles in a row above each of the supply air shafts for horizontal air discharge,

– a perforated screen at the housing underside for reflow of indoor air (secondary air),

– a built-in air-to-water heat exchanger with horizontal copper pipes and aluminium fins,

– L-fasteners at the housing top side for fastening to ceiling.

Technical data

Specific waterside cooling capacity: 		 W/m
(related to nominal length)

Chilled water supply temperature: 		 °C

Chilled water return temperature		 °C

Chilled water flow rate: 		 l/h

Waterside pressure drop: 		 Pa

Max. operating pressure: 	standard 6 bars 1)

Water quality: 	mains water

Indoor air temperature: 		 °C

Primary air temperature: 		 °C

Primary air flow rate: 		 l/s [m3/h]

Airside cooling capacity:		 W

Sound power level: 		 dB(A) ref. 10-12W

Pressure drop: 		 Pa

Dimensions / Type:
Installation type: 	 flush with ceiling (standard)

freely suspended (with wings)

Nominal length: 	...... mm

Nominal width: 	597 mm

Nominal height: 	300 mm

Heat exchanger: 	 two-pipe system (standard)

four-pipe system (optional)

Water connection: 	 push-in fitting, ø 15 mm

pipe end for pressing, ø 15 mm

Connection spigot ø: 	DN ..........; ........... pieces

Position of connection spigots: 	 left, Pos. ......

right, Pos. .....

endwise, Pos. 4

Screen for 2-sided discharge

Perforation pattern: 	standard Rv 8/9.6

optional .......... (A0 >=63% required)

Material: 	galvanized sheet metal powder-coated or wet painted

Colour: 	 to RAL 9010 (standard)

to RAL ..............

Make:	KRANTZ KOMPONENTEN
Type:	DK – LIG/Z

Subject to technical alterations.

——————————————————————————

1) Higher operating pressure on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de