2.5.1. 7. 	Tender text – Induction unit for mixing ventilation, for vertical parapet mounting, 
	type IG-M-SB

… units

Induction unit for mixing ventilation – for vertical parapet mounting – for cooling, heating, and fresh air supply along the facade through window parapets

Item 1

Unit with primary air connection and built-in metallic 
primary air nozzles, consisting of: 	
water heat exchanger made from copper piping with aluminium fins and separate circuits for heating and cooling; large fin spacing for easy cleaning as per VDI 6022;

condensate tank inclusive of drain with ½“ connector;

primary air box with inspection opening as per VDI 6022;

water connection on the left or right ½” external thread.

Item 2

Air outlet element with bars parallel to the facade for screening of glazed facade when cooling or heating; quick jet velocity decay without formation of discomfortable tangential air patterns.

Technical data
Primary air volume flow rate:		l/s [m3/h]
Allowable sound power level:		 dB(A) ref. 10-12 W
Pressure loss on air side:		 Pa

Cooling mode
Total cooling output:		 W
Water supply temperature:		 °C
Water flow rate:		 l/h
Pressure loss on water side:		 kPa

Heating mode
Heating output (secondary):		 W
Water supply temperature:		 °C
Water flow rate:		 l/h
Pressure loss on water side:		 kPa

Material
Housing:	galvanized sheet metal
Air outlet element:	aluminium
painted to RAL 9010 (pure white) 1) 
Heat exchanger:	copper / aluminium

(continued)

2.5.1.7. 	Tender text – Induction unit for mixing ventilation, for vertical parapet mounting, 
	type IG-M-SB

Dimensions
Nominal unit width 2):		mm
Depth:		mm
Height:		mm

Allowable operating pressure of heat exchanger:	16 bars

Make:	KRANTZ

Type:	IG - M - SB - __

– Subject to technical alteration –

- Other colours available on request

- Consult us for other sizes

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de