2.5.2.3. 	Tender text Induction unit for mixing ventilation,for horizontal floor mounting, 
type IG-M-LB

..... units
Induction unit for cooling, heating, and fresh air supply along the facade, via a raised floor.

Item 1	
Unit with primary air connection and built-in metallic primary air nozzles, consisting of:

water heat exchanger made from copper pipes with aluminium fins and separate circuits for heating and cooling; fins with large spacing for easy cleaning as per VDI 6022;

primary air box with inspection cover as per VDI 6022;

water connections built into the left part of the housing.

Item 2

Air outlet element with bars parallel to the facade for screening of window facade when cooling or heating; quick jet velocity decay without formation of discomfort-able tangential air patterns. Element designed as a stiff, walkable grille from anodized aluminium with small bar spacing and aluminium frame; free area: 62.5%, bar dimensions: 16 x 5 mm, bar spacing: 8.5 mm.

Technical data	
Primary air volume flow rate		 l/s [m3/h]
Allowable sound power level		 dB(A) ref. 10-12W
Pressure loss on air side		 Pa

Cooling mode	
Total cooling output		 W
Water supply temperature		 °C
Water flow rate		 l/h
Pressure loss on water side		 kPa

Heating mode	
Heating output (secondary)		 W
Water supply temperature		 °C
Water flow rate		 l/h
Pressure loss on water side		 kPa

Material	
Housing:	galvanized sheet metal
Air outlet element:	aluminium
 Anodized in natural colour
 painted to RAL 9006 1)
Heat exchanger:	copper / aluminium

(continued)

5.2.3. Tender text Induction unit for mixing ventilation,for horizontal floor mounting, 
          type IG-M-LB

Dimensions	
Nominal unit width 2):	.......... mm
Grille depth:	.......... mm
Height, without feet 3):	210 mm
Allowable operating pressure of heat exchanger:	16 bars

Make:	KRANTZ

Type:	IG – M – LB – __  – __

– Subject to technical alteration –

1) Other colours available on request
2) Other sizes available on request
3) Feet adjustable between 10 and 60 mm

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de