1.3.6. Tender text 1)

.......... units

Floor displacement outlet for low-turbulence horizontal, radial

supply air flow above the floor, for installation in floor tiles of conventional raised floor systems;

the air outlet can be walked over, driven over and can support a wheelchair; load class to EN 13264: ‘Heavy’;

consisting of:

- circular air outlet element with radial air slots and perforated air outlet centre,

- distributor basket in the following options:

- ‘Standard type’ with surrounding slots in basket casing, optionally fitted with throttle device for full shutoff of air outlet.

- ‘Short type’ with surrounding slots in basket casing, best for low raised floors, without throttle device.

- ‘Short type with fixed damper’ for even supply air distribution when used in assembly rooms or with low air outlet volume flow rates.

- ‘Low type’ with surrounding slots in basket casing and openable bottom, best for raised floors with thicker tiles and lower plenums, optionally fitted with throttle device.

- ‘Perforated sheet metal type’, for floor air outlets made of metal, including throttle device.

- optional clamp insert for installation in through bore of floor tile, fixed with clamp collar or claw fastener.

- optional connection box for direct connection of air outlet to a flexible duct, optionally fitted with volume flow damper adjustable from room.

The air outlet element can be optionally locked against unauthorized removal.

Material:

- Air outlet element made of aluminium in natural colour 2)

- Clamp insert made of aluminium in natural colour 2)

- Distributor basket made of galvanized sheet metal or polycarbonate

- Connection box made of galvanized sheet metal

Make: Krantz

Type: Q-B – DN 200 – ___ __ – __ – __

Subject to technical alterations.

1) For the required air outlet type (kind, material, etc.) or possible combina- tion of individual components, see Technical Selection Table 3 ‘Types available’ on page 6

2) Powder coating to RAL .... on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de