1.2.1. Tender text – Supply air outlet

.......... units

Radial slot outlet for generating high-induction radial air jets for high-quality indoor air flow with symmetrical or asymmetrical jet spread, for installation flush with the ceiling or freely suspended,

consisting of:

- Air outlet with square face and radial, linear air discharge openings, optionally with square or circular array, discharge direction optionally four sides, three sides, two sides symmetrical or two sides asymmetrical, underside of the blades almost flush with the faceplate, including central fastening screw with cover

- Connection box with integrated air outlet centre fastening, boreholes for suspension in the top suspension strips, side connection spigot, optionally with lip seal, with optional built-in volume flow damper adjustable from room

Material:

- Air outlet made of galvanised and powder-coated sheet steel, face painted in colour RAL 9010, pure white 1)

- Blades made of polycarbonate PC-GF 10, body-tinted similar to RAL 9005, jet black, or similar to RAL 9010, pure white

- Connection box made of galvanised sheet steel

Make: Krantz

Type: RL – __ – ___ / ___ – Z – __ – __ __ – ___ – _

1.2.1. Tender text – Return air inlet

.......... units

Radial slot outlet as return air inlet,

for installation flush with the ceiling or freely suspended,

consisting of:

- Air outlet with square face and radial, linear air intake openings, optionally with square or circular array, underside of the blades almost flush with the faceplate, optionally available with or without blades; including central fastening screw with cover

- Connection box with integrated air outlet centre fastening, boreholes for suspension in the top suspension strips, side connection spigot, optionally with lip seal and with built-in volume flow damper adjustable from room

Material:

- Air outlet made of galvanised and powder-coated sheet steel, face painted in colour RAL 9010, pure white 1)

- Blades made of polycarbonate PC-GF 10, body-tinted similar to RAL 9005, jet black, or similar to RAL 9010, pure white

- Connection box made of galvanised sheet steel 2)

Make: Krantz

Type: RL – __ – ___ / ___ – A – __ – __ __ – ___ – _

Subject to technical alterations.

1) Other colours on request

2) On request, the connection box will be painted black inside.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de