1.1.3.3. Tender text

… units

Radial outlet for high-quality indoor air flow at minimal temperature gradients in the occupied zone, consisting of:

- low-height outlet element with spigot, specially shaped face, radial vanes – vane underside flush with surrounding outlet face – and central fastening screw with cap; outlet face is round or square

- optional volume flow collars to increase the range of volume flow rates

- optional segment cover discs for 3-way discharge or 2-way symmetric or asymmetric discharge 2)

- optional aluminium reducer (connection type A) with lateral suspension brackets and screw nut for central fastening of outlet

- optional connection box in flat design with screw nut for central fastening of outlet, with lateral suspension brackets and connection spigot, box design:

- as connection type D for radial outlet with round or square face, optionally fitted with volume flow damper adjustable from room side and/or acoustic lining.

- or as connection type F for radial outlet with square face, optionally fitted with volume flow damper adjustable from room side.

Materials:

- Radial outlet made from sheet metal powder-coated to RAL 9010 3).

- Reducer made from aluminium.

- Connection box made from galvanized sheet metal.

Make: KRANTZ KOMPONENTEN

Type: RA-N3 ….

Subject to technical alteration.

2) The segment cover discs can be turned so as to adapt the air discharge direction to the room layout
3) Other colour on enquiry

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de