1.1.8. Tender text Induction outlet IN-N-6

… units  induction outlet
with high induction effect for diffuse air flow in room with single jets at minimum temperature gradients in the occupied zone, particularly suitable for installation in suspended ceiling systems, consisting of:

Linear discharge elements with consecutive jet canals, alternately inclined at a certain angle, through which the air jet discharges at an incline alternately right and left into the room.

Discharge element made of polystyrene,
Discharge angle 45°,
Visible air outlet width 90 mm,

Standard: body-tinted deep black, similar to RAL9005
 Visible surface painted to RAL..........
 with momentum control device,

Connection box made of galvanized sheet metal, with lateral suspension brackets,
 mit akustischer Auskleidung,
 with volume flow damper in connection spigot, adjustable at spigot.
 with volume flow damper in connection box, adjustable from room.

Technical data
Volume flow rate:		 l/(s·m) (m3/(h · m))
Perm. sound power level:		 dB(A) ref. 10-12 W
Air outlet nominal length:		
Connection spigot ø:		 mm

Make:	KRANTZ KOMPONENTEN
Type:	IN – N – 6

… units blind rail
for visually streamlined air outlet rows, 
visible air outlet part corresponding to induction outlet type:

Blind rail made of polystyrene,
Visible width 90 mm,
 Standard: body-tinted deep black, similar to RAL9005
 Visible surface painted to RAL..........

Nominal length:

Make:	KRANTZ KOMPONENTEN
Type:	IN – N – 6

Subject to technical alterations.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de