1.1.9. Tender text

… units

Adjustable induction outlet 1) of small width, with high induction effect for diffuse indoor air flow and high thermal comfort in the occupied zone, well suited for installation in suspended ceiling systems, with discharge direction adjustable from horizontal to vertical as required,

for use as supply air outlet or return air inlet,

consisting of:

- linear discharge element with consecutive cylindrical and rotatable single elements for alternate air discharge to the right and to the left or one-sided air discharge, or even in closed position; 1-row to 4-row design (only 1-row design for IN-V3)

- air outlet profile for lateral attachment of false ceiling, or with lateral ceiling support profile

- connection box with endwise suspension strips and lateral bracket for stabilizing the vertical mounting position, optional volume flow damper adjustable from room; optional acoustic lining; connection box for IN-V2 optionally prepared for subsequent  mounting of diffuser element from the room

Material:

- Linear discharge element made of polycarbonate, body-tinted in black similar to RAL 9005 2) or white similar to RAL 9010 2)

- Air outlet profile made of aluminium anodized in natural colour or painted tor RAL 9010 2) pure white

- Ceiling support profile made of aluminium anodized in natural colour or painted to RAL 9010 2) pure white

- Connection box made of galvanized sheet metal

Make: KRANTZ KOMPONENTEN

Typ: IN-V ….

Blank element

… units

Induction outlet with linear discharge element and air outlet profile as described before, but without connection box, 
as blank element for continuous lines of outlets where required, open or closed at the rear; for IN-V2 optional fastening with expansion brackets

Accessories

....... units

Corner piece for outlet arrangement at 90°, to fit air outlet profile and linear discharge element as described before

… units

Endwise angle piece to fit ceiling support profile as described before, supplied loose, with boreholes and fastening screws

Make: KRANTZ KOMPONENTEN

Subject to technical alterations.

1) If the adjustable induction outlet is required for use as return air inlet, the tender text is the same as for the supply air outlet

2) Other lengths and colours on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de