1.5.1.1 Tender text

.......... units

Circular displacement outlet generating a low-turbulence supply air flow and minimal mixing of supply air with indoor air for optimum displacement of airborne particles and pollutants from the occupied zone,

consisting of:

–– a perforated cylinder with connection spigot and plain bottom, and a built-in air guiding device with orifice rings, an air deflection tube and an adjustable damper for adapting the air discharge direction to varying internal thermal loads when heating and cooling.

Adjustment of air discharge direction either manually – with Bowden cable 1), chain pull 1) or control lever on perforated cylinder – or by electric actuator or by built-in thermal control unit for automatic damper adjustment. The TS control unit adjusts the damper solely through the supply air. In applications with widely fluctuating room temperatures, the TD control unit is applied. The air outlet direction is thus controlled as a function of the temperature difference between supply air and indoor air. The piston stroke is transmitted via a rod assembly. The factory setting of the supply air control damper can be subsequently customized to local requirements through the damper settings plate.

The outlet will be either suspended above the occupied zone or placed on the floor (cylinder with finer perforations). It will be optionally fitted with fasteners for wall or pillar mounting or with two opposite L-fasteners (on the air intake side) for suspension with threaded rods or similar fixtures.

–– Option: volume flow damper with perforated blade, specially designed for the circular displacement outlet, for even air supply to several outlets connected to the same ductwork, with round casing and adapter sleeve for fitting onto the outlet housing (air intake side) and with external adjusting device.

Material:

–– Air outlet made of galv. sheet metal 2), visible outlet parts optionally painted to RAL ....

Make: Krantz

Type: VA-ZD – __ – DN ____ – __ – __ – ____ – __

Subject to technical alterations.

1) For placement at 3 m above the occupied zone; any other discharge height is to be specified in the related enquiry and/or order

2) Stainless steel upon request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de