1.5.2. Tender Text Rectangular displacement outlet VA-RN / - with adjustalbe device VA-RV

… units
Rectangular displacement outlet for installation on or directly above the floor, with low induction effect and minimal mixing of supply air and indoor air, for optimum displacement of pollutants from the occupied zone;

adjustable option available for large coverage with warm supply air (heating mode), adjustment either manually or with electric actuator,

consisting of:

- rectangular housing with small depth and built-in air guide; discharge surface made of finely perforated sheet metal with built-in twist outlets,

- connection spigot with flange,

- with manual or electric adjustment device to alter the discharge direction when cooling or heating. Placement of the adjustment device either to the right or to the left 1).

Material:

- Housing with built-in parts, air inlet spigot and perforated front plate made of galvanized sheet metal; visible outlet parts (except twist outlets) optionally powder coated to RAL ....

- Twist outlets made of polycarbonate body-tinted in a colour similar to RAL 7037, dusty grey

Make: KRANTZ KOMPONENTEN

Type: VA-R

Subject to technical alterations.

1) If the connection spigot is situated to the left or to the right in direction of air flow, with electric adjustment the actuator has to be installed opposite the connection spigot for accessibility

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de