1.5.6. Tender text

.......... units

Conical displacement outlet for air supply from great heights with minimum mixing of the supply air with the indoor air for optimum displacement of dust particles and pollutants from the occupied zone,

for installation flush with ceiling oder freely suspended,

consisting of:

outlet housing and perforated sheet metal cylinder with conical neck generating a low-turbulence displacement flow as well as core tube and peripheral annular gap to form support jets for adjustment of jet penetration depth,

valve discs and surrounding seal for regulation of jet penetration depth, operated by electric actuator,

connection spigot for duct connection.

Material:

Outlet housing with connection spigot, perforated sheet metal cylinder with conical neck, and valve discs made of galvanized sheet metal; visible parts painted to RAL 9010, pure white, or to another RAL colour.

Make: Krantz Components

Type: VA – K – DN___ – __ – __ – ____

Subject to technical alterations.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de