1.2.1.1. Tender text Multiplex outlet FA-V

… unit

Multiplex outlet for flush installation in the upper area of a room wall, with rectangular housing; rear air connection via connection spigot 1) fitted with damper adjustable from the room side;

types available:

- Multiplex outlet for supply air with front plate fitted with round jet bundle elements, each manually rotatable for supply air jet spread as desired by altering the discharge direction; rapid decrease in jet velocity and temperature difference between supply air and indoor air.
Supply air discharge through jet bundle elements.
1-row, 2-row or staggered 2-row arrangement of jet bundle elements.
Front plate either non-perforated or perforated,

- Multiplex outlet for return air with front plate fitted with round jet bundle elements. 
Return air intake through jet bundle elements.
1-row, 2-row or staggered 2-row arrangement of jet bundle elements.
Front plate either non-perforated or perforated.

Material:

- 2-part jet bundle elements (nozzle discs) 
– Orifice disc made of polycarbonate PC-GF-10-V0 bodytinted in a colour similar to RAL 9010, pure white, or similar to RAL 9005, jet-black 2)
– Nozzle support made of acrylonitrile-butadiene-styrene ABS-V0 body-tinted in a colour similar to RAL 9005, jet-black

- Housing and front plate made of galvanized sheet metal, visible part of front plate painted to RAL 9010, pure white 2)

Make: KRANTZ KOMPONENTEN

Type: FA – VT-__ __ – __ – ___ – ___ – __

Subject to technical alteration.

1) With lip sealing on request
2) Other colours on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de