1.2.6. Tender text

.......... units

Broad multiplex outlet designed for flush mounting in the upper area of a sidewall, generating a stable and spread-out supply air stream; front plate with built-in nozzle discs generating highmomentum jet bundles and with perforations discharging supply air at low turbulence; the global supply air stream can be spread out as broadly as desired, thus rapid decrease in jet velocity and temperature difference to indoor air; air outlet available for two volume flow rate ranges,

consisting of:

- perforated front plate, available in three nominal lengths, with built-in 2-part nozzle discs in 1-row or 2-row design; each nozzle disc is manually rotatable by 360°;

- optionally the broad multiplex diffuser can be provided with a perforated design faceplate. The nozzles discs are hidden behind the perforation of the face, thereby the diffuser receives a more pleasing appearance without impairing its performance;

- connection box with open back for connection to a fan coil (FC) or with one or two spigots for connection to a flexible duct (FL) inclusive of volume flow damper.
Front plate fixed to connection box by means of a clip connection.

Material:

- Front plate made of galvanized sheet metal, face painted to RAL 9010, pure white 1 + 3)

- 2-part nozzle discs

- Orifice disc made of polycarbonate PC-GF-10-V0 bodytinted in a colour similar to RAL 9010, pure white, or similar to RAL 9005, jet-black 1 + 3)

- Nozzle support made of acrylonitrile-butadiene-styrene ABS-V0 body-tinted in a colour similar to RAL 9005, jet-black

- Perforated design faceplate made of galvanized sheet metal, painted to RAL 9010 pure white 1)

- Connection box made of galvanized sheet metal

Make: Krantz

Type: BF-V ….

Subject to technical alterations.

1) Other colours on request
3) Painted to RAL 9005 (deep black), when combined with perforated design faceplate

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de