1.2.8. Tender text – Wall slot diffuser WSD
          – for supply air or return air

.......... units

Wall slot diffuser for supply air or return air, in slim design, with high induction effect for turbulent mixing ventilation close to the wall in front of the diffuser, which results in quick decrease in temperature difference and discharge velocity and generates a low-turbulence supply air flow in the occupied zone; for installation inside or behind a two-layer gypsum board wall of 100 mm thickness 1),

for horizontal air discharge or extraction,

consisting of:

- slot element fitted with consecutive cylindrical air distribution elements preset at the factory, which can be turned in order to adjust the discharge direction; 1-row or 2-row design; slot element easy to clip into the connection box from the room side;

- connection box with lateral L-fasteners for fixing to gypsum board panels and with round spigot at the rear; optional volume flow damper adjustable from the room side; optional abrasion-resistant acoustic lining.

Material:

- Slot element profile with endwise pieces made of aluminium powder coated to RAL 9010, pure white 2), or anodized in natural colour (E6 EV1)

- Air distribution elements made of polycarbonate (PC, UL 94 V-0) body-tinted in black similar to RAL 9005 or in white similar to RAL 9010

- Connection box made of galvanized sheet metal

Make: Krantz Components

Type: WSD – __ – __ – ____ – __ – __ – __ – ___ – __

– combined supply air and return air

........ units

Combined wall slot diffuser for supply air and return air, in slim design, with high induction effect for turbulent mixing ventilation close to the wall in front of the diffuser, which results in quick decrease in temperature difference and discharge velocity and generates a low-turbulence supply air flow in the occupied zone; for installation inside or behind a two-layer gypsum board wall of 100 mm thickness 1),

with a supply air and a return air segment, for horizontal air discharge and extraction,

consisting of:

- slot element fitted with consecutive cylindrical air distribution elements preset at the factory, which can be turned in order to adjust the discharge direction; 1-row or 2-row design; slot element easy to clip into the connection box from the room side;

- connection box with lateral L-fasteners for fixing to gypsum board panels, with separate segments for supply air and return air and with round spigots at the rear; optional volume flow damper adjustable from the room side; optional abrasionresistant acoustic lining.

Material:

- Slot element profile with endwise pieces made of aluminium powder coated to RAL 9010, pure white 2), or anodized in natural colour (E6 EV1)

- Air distribution elements made of polycarbonate (PC, UL 94 V-0) body-tinted in black similar to RAL 9005 or in white similar to RAL 9010

- Connection box made of galvanized sheet metal

Make: Krantz Components

Type: WSD – K – __ – ____ – __ – __ – __ – ___ – __

Subject to technical alterations.

1) Other wall thicknesses on enquiry

2) Other colours on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de