2.5.1.8. Tender text – Induction unit for displacement ventilation, for vertical parapet mounting, type IG-Q-SB

… units

Induction unit for displacement ventilation – for vertical parapet mounting – for cooling, heating, and fresh air supply along the building facade through window parapets.

Unit to be integrated into the existing parapet cover, with primary air connection and built-in metallic primary air nozzles, consisting of:

water heat exchanger made from copper piping with aluminium fins and separate circuits for heating and cooling; large fin spacing for easy cleaning as per VDI 6022;

condensate tank inclusive of drain with ½” connector;

primary air box with inspection opening as per VDI 6022;

displacement air outlet for discharging supply air – made up of a blend of primary and secondary air – at low turbulence and low momentum, according to the principle of displacement ventilation.

Primary air connection (as seen from the unit front) 
 on the left  on the right, 
water connection on the right
 with control valves
 with L-fasteners for mounting the unit on the wall, adjustable in two planes.

Technical data
Primary air volume flow rate:		 l/s (m3/h)
Allowable sound power level:		 dB(A) ref. 10-12W
Pressure loss on air side:		 Pa

Cooling mode
Total cooling output:		 W
Water supply temperature:		 °C
Water flow rate:		 l/h
Pressure loss on water side:		 kPa

Heating mode
Heating output (secondary):		 W
Water supply temperature:		 °C
Water flow rate:		 l/h
Pressure loss on water side:		 kPa

Material
Housing:	galvanized sheet metal
 without powder coating
 painted to RAL 9005 (jet-black)
Heat exchanger:	copper / aluminium

(continued)

2.5.1.8. Tender text – Induction unit for displacement ventilation, for vertical parapet mounting, type IG-Q-SB

Dimensions
Nominal unit width 1):		 mm

Depth:	160 mm
Height:	680 mm

Allowable operating pressure of heat exchanger:	16 bars

Make:	KRANTZ KOMPONENTEN

Type:	IG – Q – SB

– Subject to technical alteration –

1) nur bei Nennbreiten 290 und 500

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de