1.3.7. Tender text

.......... units

Floor displacement outlet, circular, for low-turbulence radial and horizontal supply air distribution over the floor,

consisting of:

- floor insert with specially shaped carpet protection ring and four claw fasteners,

air discharge element with surrounding radial slots and central recess (4.5 mm deep) for accommodating a piece of carpet,

volume flow rate throttle for stepless manual adjustment from above during commissioning,

- accessory: plastic lid to close the cental recess.

Material:

- Air outlet made of polycarbonate, outer surfaces scratch resistant, with matted finish; colour similar to RAL 7037 (dusty grey).

Make: Krantz Components

Type: Q-B – DN 215 – D – ___

Subject to technical alterations.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de