1.1.3.1. Tender text 1)

… units 
Radial outlet for high-quality indoor air flow with minimal temperature gradient in the occupied zone,

consisting of:

air outlet element with short spigot and radial vanes – vane undersides flush with surrounding face area –, either with circular face for various ceiling mounting options or with square face with turnup for mounting in square tile ceilings, and with central fastening screw with cap;

connection to the duct system either via a reducer fitted with opposite L-suspensions or via a flat connection box with connection spigot, central fastener for fixing the air outlet, and flange bores for suspension; connection box optionally fitted with volume flow damper adjustable from the room or – only for connection type E – at the spigot; optional acoustic lining.

Materials:

- Radial outlet made of galvanized sheet metal, powder coated to RAL 9010, pure white, or RAL ....

- Reducer made of aluminium

- Connection box made of galvanized sheet metal

Make:	KRANTZ KOMPONENTEN
Type:	RA – N

Subject to technical alterations.

1) This tender text also applies in case the radial outlet is used as a return air inlet

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de