1.1.6.3. Tender text Variable twist outlet with jet straightener DD-VG

.......... units

Variable twist outlet for air supply from great discharge heights, with high-induction radial air jets and discharge direction adjustable from horizontal to vertical down, suitable for cooling and heating with great temperature differences between supply air and return air,

consisting of:

outer cylinder with round intake for connection to a circular duct, core chamber, rounded exit, and twist vanes fixed between

outer cylinder and core chamber; with adjustable jet straightener for discharge heights of 3 to 28 m; adjustment either manually or with electric actuator.

Connection to the duct system either directly to a circular duct to EN 1506, with L-fasteners, or via a connection box with connection spigot.

Material:

- Air outlet made of aluminium powder coated to RAL ….

- Connection box made of galvanized sheet metal

Make: Krantz

Type: DD - VG

Subject to technical alteration.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de