1.6.3. Tender Text Step displacement outlet Q-SL and Q-SR

… units,
 Linear step displacement outlet, type Q–SL,
 Circular step displacement outlet, type Q–SR,
for installation in a step cutout or bore, designed for low-turbulence, draught-free fresh air supply to the occupied zone,
consisting of:
finely perforated frontal plate to generate low-turbulence discharge flow according to the principle of displacement ventilation,
perforated intake or fixed throttle for even air supply, especially when several outlets are connected to the floor plenum,

Type Q–SL
Air intake from pressurized plenum, intake at  the back,  the bottom of the outlet, jet straightener to raise jet on discharge side,
 with frame and  screws,  claw fasteners  1),
 without frame, with fixing brackets for push-in connection,
skirting seal for ensuring airtightness.

Technical data
Volume flow rate:		 l/s (m3/h)
Perm. sound power level:		 dB(A) ref. 10-12 W
Pressure loss:		 Pa
Height / Length:	120 mm2) / 	 mm

Step displacement outlet: 	Galvanized sheet metal

Visible part painted to RAL

Jet straightener: 	Polycarbonate PC GF 10, dark grey

Make:	KRANTZ KOMPONENTEN
Type:	Q - SL

Accessories:
 … units
Template for fastening type B (with fixing brackets)

---------------------------------------------------------------------------------------------------------------

Type Q–SR

Air intake from pressurized plenum, skirting seal at the back of the exit flange to ensure airtightness,
concealed hexagon socket screws at claw fasteners.

Technical data
Volume flow rate:		 l/s (m3/h)
Perm. sound power level:		 dB(A) ref. 10-12 W
Pressure loss:		 Pa
Size:	DN

Step displacement outlet:	Galvanized sheet metal

Visible part painted to RAL

Make:	KRANTZ KOMPONENTEN
Type:	Q – SR

– Subject to technical alterations –

- Colourless cap; RAL colour on request

- Other heights on request

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de