1.4.5. Tender text

… units

Wall displacement outlet for low-turbulence air flow according to the principle of displacement ventilation, for mounting in room walls at ceiling height, with finely perforated faceplate for air discharge.

Type

- Linear wall displacement outlet with rectangular housing, circular connection spigot, jet straightener, and perforated faceplate; option: volume flow damper adjustable from room.

- Circular wall displacement outlet with circular housing with exit flange, connection spigot, intake throttle, and perforated faceplate; fastening via claw fasteners or lip seal.

- Combined wall displacement outlet with rectangular housing divided into supply and return air segments with thermal partition, with connection spigots for supply air and return air, and perforated faceplate; option: volume flow damper adjustable from room.

Material:

Wall displacement outlet made of galvanized sheet metal. Faceplate and exit flange 2) painted to RAL ....

Make: KRANTZ KOMPONENTEN

Type: Q-w_....

Subject to technical alterations.

2) For circular wall displacement outlet

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de