1.4.6. Tender text Ceiling displacement outlet

- non-adjustable Q-DN
	- adjustable Q-DV

… units
Ceiling displacement outlet for vertical, low-turbulence air supply and intensive flushing of occupied zone,

K1) adjustable with support jet for high penetration depth also with warm supply air (heating mode),
consisting of:

housing with square or rectangular perforated, removable air discharge element and circular connection spigot, 
       lateral,  above,
 K1) built-in core tube to generate support jet, with valve disk for support jet regulation to alter jet penetration depth, 
implants for an optimum jet pattern.

Technical data
Volume flow rate:		 l/s (m3/h)
Adm. sound power level:		 dB(A) ref. 10-12 W

K1)	valve disk adjustment
	 manual.
	 with electrical servomotor.

Material:	galvanized steel

Visible air outlet element painted to: RAL …..

Make:	KRANTZ KOMPONENTEN
Type:	Q – D

– Subject to technical alterations –

K1)  Cross for adjustable ceiling displacement outlets

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de