1.7.1. Tender text

.......... units

Volume flow controller with built-in electronic control system for use in circular supply air and return air ducts of HVAC systems,

consisting of:

- circular housing suitable for two-side connection to ducts to EN 1506 and flexible ducts to EN 13180; also suitable for flange connection to EN 12220; damper blade with internal silicone seal 1) for full shutoff,

- air tightness category 3 to EN 1751

- housing leak tightness fulfils category B to EN 1751

- optional insulating shell to reduce sound radiation and for thermal insulation

- Belimo compact controller, type LMV-D3-MP (up to DN 250) or NMV-D3-MP (from DN 315 upwards), with integrated volume flow sensor, actuator and measurement recording device

- performance range either L6, L10 or L13

- operating range either 0 – 10 V or 2 – 10 V 2)

- service port for connecting service and diagnosis tools

Factory-setting of required volume flow rates; resetting possible.

For use in CAV systems or VAV systems with

max. volume flow rate: .................. l/s [m3/h] 3)
min. volume flow rate: .................. l/s [m3/h] 3)

Material:

- Housing made of galvanized sheet metal

- Measuring cross made of aluminium/plastic (PS)

- Damper blade seal made of silicone

- Insulating material is mineral wool, covering is made of galvanized sheet metal

Make: Krantz Components

Type: VRI – DN ____ – __ – __ – __

Subject to technical alterations.

________________________________________________________________________________________________________

1) Other material on request

2) Standard setting 2 – 10 V. If you wish 0 – 10 V, please specify it in your order.

3) Unless otherwise specified in the order, the setting min. volume flow rate = 0 and max. volume flow rate = limit volume flow rate 
    will be supplied

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de