1.2.2. Tender text Linear whirl outlet (for WL-1, WL-2, WL 3)

… units

Linear whirl outlet to generate high-induction air jets for turbulent mixing ventilation,

consisting of:

- a rectangular discharge element with several discharge chambers for one-way air discharge, designed for connection to a rectangular duct, with perforated plate for uniform air flow; placement either singly or consecutively in rows; on request the bottom of the discharge element can be additionally fitted with 3 twist outlets;

- an optional connection box which is optionally available with acoustic lining and volume flow damper adjustable from room

Material:

- Discharge element and support bracket made of galvanized sheet metal, desired colour RAL ….

- Connection box and perforated plate made of galvanized sheet metal

- Twist outlets made of polystyrene on request

Make:	KRANTZ KOMPONENTEN
Type:		WL

1.2.2. Tender text Linear whirl outlet (for slim type)

… units

Slim linear whirl outlet to generate high-induction air jets for turbulent mixing ventilation,

consisting of:

- a rectangular discharge element with several discharge chambers for one-way air discharge,

- a low-height connection box fitted either with rear connection spigot (length … mm x height … mm), optionally available with volume flow damper adjustable from room, or with a rear perforated metal screen for outlet connection to a pressurized plenum

Material:

Discharge element and connection box made of galvanized sheet metal

Make:	KRANTZ KOMPONENTEN
Type:	  WL

Subject to technical alterations.

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de