1.2.3.2 Tender text Twist nozzle, type DW-V2-...-DR

… units

Swivel jet nozzle with rounded intake featuring good aerodynamic and acoustic properties, housed in a hemispheric casing with opposite swivel bearings, swivel range ± 30°, designed as twist nozzle 1) with small jet penetration depth for air distribution

into narrow spaces, with built-on twist element,

fitted with:

fastening flange to accommodate the hemisphere and the nozzle, turnable within slot segments for setting the discharge direction as required; a scale with 10-degree division helps set the discharge direction accurately when tuning the HVAC system. The discharge direction can be adjusted manually, by electric actuator or, without auxiliary energy, by a self-acting thermostatic control unit. With thermostatic control unit, the factory-set swivel range can be altered manually once the swivel jet nozzle is installed; this is possible in increments of 5° and up to 20˚ in total. The mechanism of the thermostatic control unit is protected from undue application of force by a device that can disengage and engage again when the nozzle is swivelled by hand.

- Connection type K with flange for connection to a pressurized plenum or a rectangular duct, inclusive of collar to conceal the fastening screws.

- Connection type R with push-in end for insertion into a circular duct to EN 1506, with seal.

- Connection type F with slip-on end for shaped parts to EN 1506.

- Connection type B with connector for flexible duct.

Material:

- Nozzle body and collar made of aluminium in natural colour or painted to RAL ....

- Push-in and slip-on ends made of galvanized sheet metal

- Twist element 1) made of galvanized sheet metal, black-painted

Make:	KRANTZ KOMPONENTEN
Type:	DW–V2–….-DR

Subject to technical alternations

1) Available in DN 80 up to DN 250

Krantz GmbH
Uersfeld 24, 52072 Aachen, Germany
Phone: +49 241 441-1, Fax: +49 241 441-555
info@krantz.de, www.krantz.de